## Slide 1: Step Code for Part 9 Buildings: Process and Case Studies
Notes: Presented by E3 Eco Group, Einar Halbig will offer real time examples, showing how builders are achieving Step Code Levels 2 and 3.
You have probably heard about the “Step Code” by now, but perhaps are not clear about when it will take effect and how it might change how you approach house construction.
This seminar will provide background information on the BC Provincial Step Code, and also will show how the Step Code applies to a particular house we’ll look at as a case study. We will see how certain combinations of envelope upgrades and changes to the mechanical system will affect the Step Code metrics for this house, and how that relates to other houses. We will also review the air tightness requirements of Step Code and provide recommendations of how best to reach those targets. By the end you should have a much better idea of what Step Code will mean to you and how you might reach Step Code levels.
Take-aways:
understand what Step Code is, and what buildings it applies to
understand the Step Code metrics
understand how particular upgrades affect Step Code metrics
understand air barriers, airtightness testing and how to achieve the Step Code requirements for air tightness

## Slide 2: Agenda:
Conclusion
Step Code review
Understanding the Step Code “metrics”
Who are/working with an Energy Advisor
Case study- getting a house to Step 1, 2 and 3
Case study- getting a rowhouse to Step 1, 2 and 3
Wrap up and questions.

## Slide 3: Audience Experience with Energy Efficiency
Who knows the basics of the Energy Step Code?
Who has worked with an Energy Advisor before?
Who had a blower door test done on a project and what was the result?
Did you ever have to meet certain energy targets?
What questions would you like answered?

## Slide 4: Two Provincial Initiatives Led to the BC Step Code
Building Act
Consistency, Competency & Innovation
December 2017 marks the end of local building requirements in bylaws.
Climate Leadership Plan
Establishes a target that all new construction will be net-zero ready by 2032.
Notes: Why are we here today?
Two provincial document are drivers for the Energy Step Code:
The Building Act: no more possible for local government to adopt their own requirements and approached for building energy efficiency.
Climate Leadership plan: all new construction will be net-zero ready by 2032.
Speaker to ask audience to keep the 2032 date in mind. Mention that the date will re-appear in a few slides.

## Slide 5: Where does Step Code fit in?
BCBC Section 9.36 Energy Efficiency
  9.36.2 Building Envelope
  9.36.3 HVAC Requirements
  9.36.4 Service Water Heating Systems
  9.36.5 Energy Performance Compliance
  9.36.6 Energy Step Code
Energy Modeling only: energy targets and air tightness
Energy Modeling: Ref. vs. Proposed
Prescriptive

## Slide 6: Which Buildings?
All Part 9 Buildings:
  Single family houses
  Rowhouses
  Small apartment buildings (up to 3 storeys, 600sq m footprint)
  All Part 3 Buildings
  Focus today on Part 9 Buildings.

## Slide 7: BC Energy Step Code
EnergyStar for New Homes
R2000
Passive House

## Slide 8: Timing?
No need to panic.

## Slide 9: BC Energy Step Code
Mandatory December 2020?
Mandatory December 2026?
Mandatory December 2032?
Beginning December 2017: voluntary adoption

## Slide 10: Who Has Announced Intent to Adopt BC Energy Step Code
Campbell River Comox Valley RD Duncan Langley Township New Westminster North Saanich District North Vancouver City North Vancouver District | Richmond Saanich District Squamish District Surrey Victoria West Vancouver Whistler RM
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 11: Key Components of the BC Energy Step Code
  Performance Requirements For:
  Air-tightness Testing
Notes: And finally, last but not least:
Airtightness
Speaker might want to mention that the air tightness is linked to the “Envelope-first approach”.

## Slide 12: Metrics – Airtightness: Air Changes Per Hour (ACH)
Air Changes per Hour at 50 Pascal: ACH@50Pa

## Slide 13
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 14: Key Components of the BC Energy Step Code
Performance Requirements For:
Air-tightness Testing
Equipment & Systems
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 15: Equipment & Systems
“% Better than Reference House” (excluding lighting and appliance loads):
Energy Advisor inputs the “Proposed” house
HOT2000 software automatically creates the “Reference” house
Same size, shape and location of house, with same “type” of mechanicals
Section 9.36 Prescriptive minimum RSI values
2.5ACH@50Pa
maximum 22% FDWR.
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 16: Equipment & Systems
VS.
Reference house- Code minimum
Proposed house- Builder specs
“% Better than Reference House” (excluding lighting and appliance loads):
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 17: Equipment & Systems
Mechanical Energy Utilization Intensity:
Sum of energy for space heating, cooling, domestic hot water and ventilation- per year
Per sq meter of heated floor area
MEUI.
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 18: Equipment & Systems
On-site Renewable Energy Generation?
NOT included in MEUI.
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 19: Key Components of the BC Energy Step Code
Performance Requirements For:
Equipment & Systems
Air-tightness Testing
Building Envelope

## Slide 20: Building Envelope
Thermal Energy Demand Intensity:
Annual heat energy needed
After accounting for internal heat gain and solar heat gain
Per sq meter of heated floor area
TEDI.
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 21: Building Envelope
Peak Thermal Load:
Design heat load for the house (in Watts)
Per sq meter of heated floor area
PTL.
Notes: The equipment found inside the building will also have an impact on the energy performance of the building.
Note that for Part 9 buildings “Equipment and Systems” only covers DHW, heating and ventilation. Lighting and plug loads are not included. Also note that Part 3 (residential) buildings “Equipment and Systems” include DHW, heating, ventilation AND lighting + plug loads.

## Slide 22: Performance Compliance: Lower Mainland (except City of Vancouver)
 | N/A |  | ERS%<REF not less than 0% |  |  |  |  |  | 
 | 3.0 |  | -10% | OR | 60 |  | 45 | OR | 35
 | 2.5 |  | -20% | OR | 45 |  | 40 | OR | 30
 | 1.5 |  | -40% | OR | 35 |  | 25 | OR | 25
 | 1.0 |  | N/A |  | 25 |  | 15 | OR | 10
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 23: Working with an Energy Advisor
Energy modeling
Air-Tightness Testing
No More Prescriptive Requirements
BC Energy Step Code = Performance Compliance
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 24: Working with an Energy Advisor
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 25: Working with an Energy Advisor
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 26: Where to find an Energy Advisor
Conclusion
NRCan website
CHBA BC is a Service Organization
CACEA.ca is Energy Advisor association.

## Slide 27: Who are the Energy Advisors?
Conclusion
Deal with Part 9 buildings
Usually have construction background
Deal with energy modelling, upgrade suggestions, blower fan testing and paperwork
Trained by Service Organizations
Registered by NRCan
Subject to Code of Ethics and Quality Assurance process
Can be de-registered.

## Slide 28: Who are the Energy Advisors?
Conclusion
NOT a Professional designation
NOT replacing the Envelope Engineer
NOT replacing the Architect or Designer
Typically consult on upgrading construction specifications only (not design).

## Slide 29
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 30: Working with an Energy Advisor
Conclusion
Engage your Energy Advisor
Model your house and check performance against Step Code targets
Run iterations and develop your plan of action
Stick to the plan
Energy Advisor confirms the plan (blower fan test and as-built energy model).

## Slide 31: 1: Engage An Energy Advisor
Energy Advisors:
Licenced by NRCan
Construction knowledge
Trained to use HOT2000 software and blower fan testing
Standard modeling and testing procedures through EnerGuide Rating System
QA by Service Organization and NRCan.
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 32: Energy Modeling Process:
Submit drawings for your proposed house to EA
Submit all the other information to EA
EA will produce HOT2000 energy model of “proposed house”
HOT2000 will automatically create the “reference house” and compare
HOT2000 generates output values used to calculate MEUI, TEDI and PTL.

## Slide 33: Info needed for Energy Modeling:
Drawings are just the start…
Also need:
space heating specifications (type and AFUE)
domestic hot water heating specs (type and EF)
window specs (USI and SHGC)
ventilation specs (equipment and SRE if HRV)
space cooling specifications.

## Slide 34: 2: Energy Advisor Models the Building
Performance Compliance
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 35: HOT2000 Software
HOT2000 outputs used to calculate Step Code Metrics:
% lower energy than reference house
MEUI
TEDI
PTL
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 36: 3: Energy Advisor & Builder Develop Plan of Action
HOT2000 iterations evaluate potential upgrades:
Envelope upgrades (insulation, fenestration, air tightness, thermal bridging, etc)
Mechanical system upgrades
Heat recovery
Lighting and appliances?
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 37: Which upgrades make sense?
Effect on Step Code metrics?
Cost?
Availability?
Constructability?
Synergies?
Builder preference
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 38: Plan of Action:
Everything (except renewables, lighting and appliances) is on the table for upgrading:
windows
exterior walls and foundations
roofs/ceilings
air tightness
space heating system
domestic hot water heating system
ventilation system
space cooling system
drain water heat recovery.

## Slide 39: One “Wildcard”:
How airtight will the finished house be?
EAs can help with air barrier suggestions
Mid-construction blower fan testing
Builder and Trades demonstration/training
Then the final blower fan test.

## Slide 40
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 41
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 42: 4: Builder completes house, Energy Advisor confirms construction details
Make sure you build what you agreed on!
If changes, notify your Energy Advisor
The energy model will need to be updated.
Energy Advisor completes Step Code compliance forms and submits to the Municipality.
Notes: To meet the requirements of a given step of the BC Energy Step Code, a builder needs to prove to building officials that the building meets or exceeds a set of defined metrics.
The measurement and verification requirements include:
  Energy modelling: Prior to construction, builders must commission an energy model for their proposed building. This is already common practice for high-efficiency buildings in BC, and is already an optional compliance path for meeting the energy efficiency requirements in the existing BC Building Code.
  Airtightness testing: An energy advisor must complete a blower door test for all steps and all building types after construction and before occupancy.
  While a blower door test is only required before the building is complete pre-construction, it may also be helpful at a mid-point inspection to ensure any leaks in the envelope are repaired before drywall is in place.
  Again, this approach eliminates the prescriptive energy-related requirements of the BC Building Code. Instead of prescribing what builders and developers need to do to, it tells them the level of performance they need to reach, and puts the ball in their court on how to do it.

## Slide 43: Case Studies

## Slide 44: Step Code- builds upon current process:
Builder
Energy Advisor
Municipality
House
Architect
Trades
Energy Code
Step Code
already have this:
add this:

## Slide 45: Example- How to Get This House to Steps 1-3:

## Slide 46: Step by Step:
Where am I starting?
How do I get this particular house to Step 1, Step 2, Step 3?
Which climate zone am I in?

## Slide 47: Energy Modelling:

## Slide 48: Energy Modeling Results:

## Slide 49: Step 1- Enhanced Compliance:
For this house, initial choice of construction details met Section 9.36 minimums
But EnerGuide Rating is higher than the reference house
Need to get house down to the reference house value- what to upgrade?
What will the airtightness be once the blower fan test is performed?

## Slide 50: Step 1- Enhanced Compliance:
Upgrade boiler to 94% AFUE
Assume Builder can achieve air tightness of 3.5ACH@50Pa- use another value if appropriate
EnerGuide Rating is now same as the reference house.

## Slide 51: Step 1- Enhanced Compliance:

## Slide 52: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
No min. value

## Slide 53: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
“Envelope First” approach
Upgrade air tightness to required 3.0ACH@50Pa
Next easiest upgrade? Windows? Upgrade to USI 1.60
Check the effect.

## Slide 54: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
(83-78)/(83-25.4) = 8.7%
Remember Step Code says the “% better than reference house” excludes electrical base loads

## Slide 55: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
Need more improvement
“Envelope First” approach
Favour reliable/achievable upgrades- with Builder feedback to keep costs in check
Upgrade R20 wall insulation to R22
Check the effect.

## Slide 56: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
Not good enough
Upgrade R40 attic insulation to R50
Upgrade windows to USI 1.40- what about SHGC?
Check the effect.

## Slide 57: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
(83-74)/(83-25.4) = 15.6%
Remember Step Code says the “% better than reference house” excludes electrical base loads

## Slide 58: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
What about TEDI?
Thermal Energy Demand Intensity (kWh/sq m/year)
Need to reach 45kWh/sq m/year.

## Slide 59: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
40663MJ = 11,295kWh
11,295kWh/209sq m = TEDI 54

## Slide 60: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
8014W/209sq m = PTL 38
Maybe we can comply with PTL?

## Slide 61: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
Run more upgrade scenarios until all Step Code 2 parameters are met
Focus efforts- remember that only an envelope improvement will lower TEDI and PTL.

## Slide 62: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
Check HOT2000 outputs to steer direction:

## Slide 63: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
Add 1.5” expanded polystyrene to 2x4 R14 foundation wall
Check the results.

## Slide 64: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
27885MJ = 7,746kWh
7,746kWh/209sq m = TEDI 37.1

## Slide 65: Step 2- 10% better/MEUI 60 and TEDI 45/PTL 35:
7125W/209sq m = PTL 34.1
Do we also need to comply with PTL?

## Slide 66: Step 3- 20% better/MEUI 45 and TEDI 40/PTL 30:

## Slide 67: Step 3- 20% better/MEUI 45 and TEDI 40/PTL 30:
Upgrade air tightness to required 2.5ACH@50Pa for Step 3
Which additional upgrades? Already have R22, R50, USI 1.40/SHGC 0.50
We already know we are good for TEDI; it was 37.1 in our last example
We were close to “20% better than” in our last example
So we can get away with improving mechanicals, not envelope.

## Slide 68: Step 3- 20% better/MEUI 45 and TEDI 40/PTL 30:
Upgrade mechanical system with HRV (70% SRE)
Check results.

## Slide 69: Step 3- 20% better/MEUI 45 and TEDI 40/PTL 30:
(83-65)/(83-25.4) = 31.3%
Remember Step Code says the “% better than reference house” excludes electrical base loads

## Slide 70: Step 3- 20% better/MEUI 45 and TEDI 40/PTL 30:
(18.74GJ + 19.67GJ + 0.97GJ)/209 sq m = 52.3
MEUI?

## Slide 71: Step 3- 20% better/MEUI 45 and TEDI 40/PTL 30:
17697MJ = 4,916kWh
4,916kWh/209sq m = TEDI 23.5
What about TEDI?

## Slide 72: Example- How to Get This Rowhouse Building to Steps 1-3:

## Slide 73: Energy Modelling:

## Slide 74: Step Code for Rowhouses:
For rowhouses, Step Code requires the building be modelled as a whole and blower fan tested as a whole
Vs. EnerGuide which requires each rowhouse unit be modelled and blower fan tested
HOT2000 will still be used, but in “General” mode and with some adjustments
Blower fan testing is more complicated.

## Slide 75: Step Code for Rowhouses:
With Step Code, the energy model for a rowhouse building considers it a big house with a lot of occupants
More credit for internal heat gain, but also more envelope area
Generally easier to get a larger building to a particular ACH@50Pa value.

## Slide 76: Step Code for Rowhouses:
In General mode, no “% better than Reference house”
Use MEUI instead
Possible to manually generate a Reference house model for Step Code level 1.

## Slide 77: Step 1- Enhanced Compliance:
Typical rowhouse construction specs
Assume Builder can achieve air tightness of 3.5ACH@50Pa- use another value if appropriate
Reference house does not apply, and no Level 1 MEUI criteria.

## Slide 78: Step 2- MEUI 60 and TEDI 45/PTL 35 :
(214,533MJ)/1008 sq m = MEUI 59.1 kWh/sq m a
What about MEUI?

## Slide 79: Step 2- MEUI 60 and TEDI 45/PTL 35:
132,398MJ = 36,777kWh
11,295kWh/1008sq m = TEDI 36.5
What about TEDI?

## Slide 80: Step 2- MEUI 60 and TEDI 45/PTL 35:
26,098W/1008sq m = PTL 25.9
Do we also need to comply with PTL?

## Slide 81: Step 3- MEUI 45 and TEDI 40/PTL 30:
Upgrade air tightness to required 2.5ACH@50Pa for Step 3
MEUI drops to 57.6 kWh/sq m a
TEDI and PTL already ok
What to upgrade to lower MEUI?
Mechanicals!
Where to go beyond electric baseboard heaters and DHW?

## Slide 82: Step 3- MEUI 45 and TEDI 40/PTL 30:
Upgrade ventilation to 85% HRV (one per unit)
Add drain water heat recovery systems (one per unit)
MEUI drops to 44.4 kWh/sq m a
TEDI and PTL already ok.

## Slide 83: Heat Pumps and Step Code:
Remember Step Code metrics include cooling load, if cooling is “needed” and possible in the house
Heat pump means cooling is possible
Heating energy goes down, but cooling energy is introduced- how does MEUI change?
Be cautious of heat pumps combined with high Solar Heat Gain windows.

## Slide 84: Blower Fan Testing a Rowhouse for Step Code:
Option 1: Test the whole rowhouse building using 6 fans simultaneously.

## Slide 85: Blower Fan Testing a Rowhouse for Step Code:
Option 2: Builder leaves openings in party walls so whole rowhouse building is tested using 1 fan.

## Slide 86: Blower Fan Testing a Rowhouse for Step Code:
Option 3: “Guarded” blower fan testing of each unit and add the results.

## Slide 87: Blower Fan Testing an Apartment Building for Step Code:

## Slide 88: Questions?