## Slide 1: Building Envelope Retrofit Abroad: Parallels with New Zealand and Different Perspectives
BCBEC 2024: Renew. Restore. Reinvent. Extending the Legacy of Existing Buildings

## Slide 3: My Journey
My Background
Started my career in 2007 in BC (P.Eng)
Relocated to Seattle in 2014 (P.E.)
In 2016, made the move to Auckland (CPEng)
2018 Founded Oculus Architectural Engineering Ltd.
Team of 20 - 10 of which are Canadian

## Slide 4: My Journey
Why New Zealand?
Some previous building science stuff happening in NZ
Transferable skills and qualifications
Friendly immigration policies – Working Holiday Visa
Great weather
Less MAGA
Impact

## Slide 5: Climate

## Slide 6: Leaky Homes

## Slide 7: Seismic

## Slide 8: Key Insulation Milestones

## Slide 9: Key Insulation Milestones
1978 - First building code requirement for insulation
2007 - Double glazing,
- R1.9 wall,
- R2.9 roofs
- Thermally broken window frames,
- R2.0 Walls
- R6.6 Roofs

## Slide 10: Uninsulated Houses
>800,000 or 55% of homes in NZ are uninsulated
Roof and floor insulation is considered a selling feature
Chronically underheated or unheated

## Slide 11: Average Energy Use
Average NZ House:
8,500 kWh / year total energy use (TEUI Actual)
Average house 175 square metres
~ 50 kWh / sqm *yr
$2,500 / year
Heating and Cooling:
~15% = 7.5kWh/sqm*yr (TEDI Actual)
~45kWh/sqm*yr predicted
Friendly climate and cultural norms overestimate energy use significantly
Houses are not maintained at 20C
No code requirement for heating

## Slide 12: Asthma

## Slide 13: Asthma

## Slide 15
The internet is only 1 generation old
Culture is still dominated by ‘what’s available’ mentality
Number 8 wire
Preference for what’s been done before or readily available
Number 8 Wire

## Slide 16
90X45 (2X4)
Radiata Pine
H1.2 treated
Nogs and Dwangs
Sheathing optional (bracing)
No vapour barriers
Prenail (offsite modular)
R2.0 (R11.35)
Timber Frame Walls

## Slide 17
>~90% of new houses start in a ‘factory’ setting
Walls and trusses
Prenail Frame and Truss

## Slide 18
>90% of roofs are metal
<5% asphalt shingles
<5% membrane roofs
Metal on battens
Absorbent underlay
Safety mesh
Roofing

## Slide 20
>90% of windows are aluminium
Until 2024 these were non-thermally broken
Double glazed
Window reveals are stapled to the frame
Supported by WANZ bar
Windows

## Slide 22
Air source heat pumps are the primary heating source for new homes
Provides cooling too
Some intermittent exhaust fan requirements
Minimum window opening sizes
HVAC

## Slide 23: Same Answer to Different Questions

## Slide 24: Building for Climate Change

## Slide 25: Operational Efficiency Caps
2026 2028 2030
= Passive House
= Current Industry Standard (w heat pumps) (TEDI)

## Slide 26: NZ Challenge

## Slide 27: Where to Find Us?